MECHANICAL SEAL ORDER DATA SHEET (ALL FIELDS ARE MANDATORY)

| Customer, address: |  |
| --- | --- |
| Contact person: |  |
| Position: |  |
| P.O.box: |  | Telephone: |  | e-mail: |  |

| Quantity |  |
| --- | --- |
| Mechanical seal type | Single |  | Double |  | Tandem |  | Bellows |  |
| Scheme according API 682 |  |
| Fitting for strapping | Need |  | No requirement |  |  |

#### Pump parameters

| Brand of the pump/Type API 610 |  |
| --- | --- |
| Pump type |
| Overhung |  | Between-bearing |  | Vertical |  | Horizontal |  | Semisubmersible |  |  |
| Rotation frequency, rpm |  |
| Direction of rotation on the engine side | Right |  | Left |  |  |
| The frequency of operation | Continuous |  | Periodic |  | Steaming/washing | Yes |  | No |  |
| Washing medium |  | Washing temperature, °С |  | Washing pressure, MPa |  |

| Class of hazard zone | 0 |  | 1 |  | 2 |  |
| --- | --- | --- | --- | --- | --- | --- |
| Explosion protection marking |  |

| Parameters | Value | Parameters | Min | Max |
| --- | --- | --- | --- | --- |
| The name of medium |  | Inlet pressure, MPa |  |  |
| Fluid composition (components). Special properties (radio-activity, explosion, fire hazard, toxicity, etc.)) |  | Discharge pressure, MPa |  |  |
|  |  | Seal chamber pressure, MPa |  |  |
|  |  | Temperature, °C |  |  |
| pH (for aqueous solutions) |  | Ambient temperature, °C |  |  |

## characteristics of the pumped medium

## design characteristics

| Dshaft | Shaft diameter (without sleeve) |  |
| --- | --- | --- |
| Dsleeve | Shaft sleeve diameter (if present) |  |
| D1 | Seal chamber diameter |  |
| L1 | Seal chamber depth |  |
| L2 | Max value of mounting distance (from seal chamber seal face to bearing of flange face) |  |
| D2 | Hole-circle diameter for bolt fastening |  |
| D3 | Max seal flange diameter |  |
| Dbolt | Bolt diameter |  |
| N | Apertures number for bolt fastening |  |

| Is sleeve removal possible? | Yes |  | No |  | Trimming is possible |  |
| --- | --- | --- | --- | --- | --- | --- |
| Features of shaft geometry (threading, grooves, ledges, etc. (within sizes L1, L2) their arrangement relatively to seal chamber seal face (to specify if required) |  |
| Is it possible to disassemble the pump to perform measurements when ordering? | Yes |  | No |  |

SIGNATURE _________________/_____________________________________________________												LS

# Text boxes

If there is a drawing (sketch) of the original mechanical seal, send it with the order data sheet